## Slide 1
EMERTXE INFORMATION TECHNOLOGIES
CAR BLACK BOX
Presented By: Anil A Halagunaki
BATCH : 24018I

## Slide 2
Contents :
Introduction
Abstract
Introduction
Purpose
Technical Specification
The Program Flow
Advantages And Application
Conclusion

## Slide 3: INTRUDUCTION
WHAT IS CAR BLACK BOX ?
A car black box, or Event Data Recorder (EDR), is a device installed in vehicles to log and store critical operational data.
Similar to an airplane's black box, it records key details such as speed, location, braking intensity, and engine performance.
This data is crucial for analyzing accidents, offering insights into vehicle behavior during incidents.
It aids insurance claims by providing objective evidence to determine fault and combat fraud.
Car black boxes enhance safety by tracking driver behavior and vehicle performance, helping to identify issues early.
They also help vehicles comply with regulatory standards for safety and data recording.

## Slide 4: ABSTRACT
Designed and developed an event recorder system for vehicles using the PIC18F4580 microcontroller, ensuring robust and reliable performance.
Integrated real-time tracking and logging of critical vehicle events, such as gear shifts, collision detection, and speed monitoring, with real-time updates displayed on a 16x2 LCD screen.
Utilized the DS1307 Real-Time Clock (RTC) for precise event timestamping and implemented external EEPROM for secure and reliable storage of logged data.
Created a user-friendly interface with an intuitive menu for viewing, clearing, and downloading logs via UART communication, enabling seamless data management.
Demonstrated expertise in embedded systems, real-time programming, and hardware interfacing, highlighting strong practical knowledge of electronics and programming.

## Slide 5: PURPOSE
Monitor Critical Events:
Log key events such as sudden braking, sharp turns, and collisions.
Offer comprehensive data for detailed post-incident analysis.
Enhance Safety:
Detect potential vehicle issues early through continuous data tracking.
Analyze driving patterns to improve driver behavior and provide actionable feedback.
Support Insurance Claims:
Supply precise data to validate insurance claims and prevent fraudulent activities.
Offer objective evidence to determine liability in accidents.
Regulatory Compliance:
Facilitate adherence to vehicle safety and data recording regulations.
Accident Investigation:
Deliver essential data for reconstructing accidents and identifying their root causes.

## Slide 6: TECHNICAL SPECIFICATION
PIC18F4580: Microcontroller for system control.
C Language: Used for programming.
MPLAB X IDE: Development and debugging environment.
16x2 LCD: Displays real-time data.
Matrix Keypad: Captures user input.
External EEPROM: Stores the last 10 events.
UART: Transfers logs to external devices.
ADC: Measures analog inputs like speed.
I2C Protocol: Connects RTC and EEPROM.
DS1307 RTC: Provides event timestamps.
Power Supply: Ensures stable operation.
PCB: Optimized hardware layout.

## Slide 7: THE PROGRAM FLOW
System Initialization
Initialize PIC18F4580 microcontroller.
Configure peripherals: CLCD, Matrix Keypad, EEPROM, UART, ADC, and I2C.
Main Program Loop
Continuously monitor and record critical events like gear shifts, collisions, and speed.
Event Detection and Logging
Detect gear shifts via GPIO inputs.
Use accelerometer data to detect collisions.
Measure vehicle speed through ADC.
Log events with RTC timestamps in EEPROM.
Display real-time data on the CLCD.

## Slide 8
User Interaction
  Capture user input via Matrix Keypad for menu navigation.
  Provide menu options: Dashboard, View Logs, Clear Logs, Download Logs, and Set Time.
Data Management
  Dashboard: Display real-time vehicle status and system info.
  View Logs: Retrieve and show the latest 10 events from EEPROM.
  Clear Logs: Erase stored events in EEPROM.
  Download Logs: Transfer logs to an external device via UART.
  Set Time: Update RTC (DS1307) with the current time.
Error Handling
  Implement mechanisms to detect and correct errors for data integrity.

## Slide 9: ADVANTAGES AND APPLICATIONS
Advantages:
Offers instant updates on critical vehicle events.
Logs important data for future analysis.
Simplifies usage with a user-friendly menu interface.
Ensures accurate event timestamps using RTC.
Allows data transfer via UART for detailed analysis.
Prevents data loss with external EEPROM storage.
Applications:
Fleet monitoring and management.
Performance tracking and issue identification.
Driver behavior monitoring and improvement.
Alerts and logs for critical incidents.

## Slide 10: CONCLUSION
The vehicle event recorder system is a robust and efficient solution for monitoring and logging critical vehicle events. Utilizing the PIC18F4580 microcontroller, it ensures real-time tracking and accurate data storage with features like an RTC for precise timestamps and an external EEPROM to prevent data loss. Its user-friendly interface, equipped with a matrix keypad and CLCD, simplifies interaction through options like viewing, clearing, and downloading logs. The system enhances safety by identifying potential issues, improving driver behavior, and providing reliable data for accident analysis and insurance claims. With its advanced functionalities, error-handling mechanisms, and seamless data transfer via UART, this project demonstrates the practical application of embedded systems in automotive technology, offering significant benefits in fleet management and regulatory compliance.

## Slide 11: THANK YOU